## Slide 1
Robotic Multi-Axis Motor Controller & Actuator Hub
Domain 5: Robotics, Edge AI & Hardware Emulation Linux Device Drivers | POSIX Real-Time Systems | Modern C++
Author: Engineering Trainee | Project Lead: Aman Kumar | 20-Day Advanced Systems Training
GitHub: https://github.com/Amankumar307/robotic-motor-hub | October 2026

## Slide 2
CAPSTONE PROJECT | DOMAIN 5
Stage 1: Project Overview & Industrial Motivation
1. Industrial Motivation
• Modern robotics (6-DoF arms, CNC gantries, AGVs) require microsecond-level synchronization across multiple motor axes.
• Stepper and BLDC motors must track synchronized trajectories without drift or lag.
• Widely applied in automated pick-and-place, CNC milling, semiconductor wafer handling, and autonomous navigation.
2. Problem Statement
• Non-deterministic latency in standard user-space Linux causes trajectory tracking error and vibration.
• Bridging high-level trajectory planning with low-level hardware registers lacks unified driver abstractions.
• Mechanical stall, encoder disconnection, or limit switch contact requires sub-millisecond emergency stop cutoffs.
3. Core Objectives
• Build a Linux Character Device Driver (/dev/motor_hub) with MMIO registers and 1 kHz hrtimer interrupts.
• Construct a deterministic 1 kHz C++ daemon scheduled under POSIX SCHED_FIFO.
• Implement anti-windup discrete PID & synchronized multi-axis trapezoidal trajectory planner.
• Create zero-copy Shared Memory IPC and real-time safety watchdogs.

## Slide 3
CAPSTONE PROJECT | DOMAIN 5
Stage 2: Project Requirements & Deliverables Matrix (PRD)
Key Functional Requirements (FR)
• FR-01: Multi-Axis Control: Up to 6 coordinated motion axes (X, Y, Z, Roll, Pitch, Yaw).
• FR-02: Linux Character Driver: IOCTL interface for atomic register read/write and batch telemetry.
• FR-03: Hardware Interrupt Simulation: 1 kHz hardware physics tick via kernel hrtimer.
• FR-04: Closed-Loop Regulation: Discrete PID control with anti-windup clamping.
• FR-05: Synchronized Profiling: All axes accelerate, cruise, and decelerate in lockstep.
• FR-06: Dual HAL: Swappable kernel driver and high-fidelity mock emulation.
Non-Functional Requirements (NFR) & Targets
• NFR-01: Control Loop Frequency: Deterministic 1000 Hz (1.0 ms period).
• NFR-02: Computation Latency: <= 150 µs loop execution time budget.
• NFR-03: E-Stop Latency: Emergency stop to PWM 0 in <= 1.0 ms.
• NFR-04: Memory Footprint: Resident memory (RSS) <= 16 MB.
• NFR-05: Zero Allocation in Periodic Loop: Pre-allocated buffers to prevent heap jitter.
• NFR-06: High Telemetry Throughput: Zero-copy POSIX Shared Memory streaming.

## Slide 4
CAPSTONE PROJECT | DOMAIN 5
Stage 3: 5-Layer Decoupled System Architecture
Layer 5: User & Operator Layer
Interactive Motor CLI Client (motor_cli) | Live 10 Hz Telemetry Dashboard
Layer 4: Inter-Process Communication (IPC)
POSIX Shared Memory (/dev/shm/motor_hub_telemetry) | Command Queue Server
Layer 3: Real-Time Motion Control Core
1 kHz Daemon (SCHED_FIFO) | MultiAxisController | PID | TrajectoryPlanner | Watchdog
Layer 2: Hardware Abstraction Layer (HAL)
IHardwareDevice Interface | KernelDeviceDriverHAL | MockHardwareEmulatorHAL
Layer 1: Kernel Driver & Hardware Emulation
motor_hub_driver.ko | Char Dev /dev/motor_hub | Sysfs /sys/class/motor_hub | MMIO Registers

## Slide 5
CAPSTONE PROJECT | DOMAIN 5
Stage 3: Hardware-Software Co-Design & MMIO Register Map
32-Bit Word-Aligned Register Map
• 0x00 - REG_AXIS_CTRL: Enable (b0), Reset (b1), E-Stop (b2), Home (b3).
• 0x04 - REG_AXIS_STATUS: Enabled, InPosition, Error, Min/Max Limits, E-Stop.
• 0x08 - REG_TARGET_POS: Desired quadrature encoder position (signed 32-bit).
• 0x0C - REG_ACTUAL_POS: Measured encoder position (signed 32-bit).
• 0x10 - REG_TARGET_VEL: Desired velocity in ticks/sec.
• 0x14 - REG_ACTUAL_VEL: Measured velocity in ticks/sec.
• 0x18 - REG_PWM_OUTPUT: Applied motor effort (-1000 to +1000).
• 0x1C-0x24 - REG_KP/KI/KD: Closed-loop gain registers (fixed-point Q16.16).
Actuator State Machine Specifications
• UNINITIALIZED: Initial boot state prior to self-test.
• IDLE: Axis initialized, drive energized, ready for commands.
• HOMING: Seeking hardware reference limit switch and zeroing tick counts.
• POSITIONING: Executing synchronized trajectory waypoints.
• JOGGING: Manual open-loop or velocity-controlled motion.
• ERROR: Tracking error stall or overtemperature tripped.
• EMERGENCY_STOP: Immediate hardware PWM cutoff latched.

## Slide 6
CAPSTONE PROJECT | DOMAIN 5
Stage 4: Linux Kernel Character Device Driver (/dev/motor_hub)
Driver Core & VFS
• Dynamic character device registration using alloc_chrdev_region() and cdev_add().
• Provides /dev/motor_hub node with custom file_operations.
• Integrates sysfs device nodes under /sys/class/motor_hub_class/.
• Allows shell-level status inspection and emergency stop override.
IOCTL Subsystem
• IOCTL_MOTOR_READ_REG / WRITE_REG: Direct MMIO register access.
• IOCTL_MOTOR_SET_CMD: High-speed target position & PWM command dispatch.
• IOCTL_MOTOR_GET_STATUS: Queries telemetry per axis.
• IOCTL_MOTOR_READ_ALL: Zero-copy batch snapshot across all 6 axes.
• IOCTL_MOTOR_TRIGGER_ESTOP: Kernel-level emergency stop latch.
Concurrency & Timers
• High-Resolution Timer (hrtimer): 1 kHz hardware physics clock.
• Physics updates: Converts PWM duty cycle to velocity and encoder tick updates.
• Thread-safe MMIO access protected by spin_lock_irqsave() in timer context.
• Process-level mutex for file open/release concurrency.

## Slide 7
CAPSTONE PROJECT | DOMAIN 5
Stage 5: Deterministic C++ Motion Algorithms
Discrete PID with Anti-Windup Clamping
• Proportional: Instantaneous reaction to position error e[k].
• Integral with Anti-Windup: Prevents integrator saturation when PWM saturates at +/- 1000.
• Filtered Derivative: Discrete low-pass filter (alpha = 0.7) eliminates high-frequency encoder quantization chatter.
• Deadband Handling: Zeroes hunting jitter when within +/- 5 ticks of setpoint.
Multi-Axis Synchronized Trajectory Planner
• Trapezoidal Velocity Profiling: Computes acceleration, constant velocity cruise, and deceleration phases.
• Triangular Profile Adaptation: Handles short moves where max velocity cannot be attained.
• Multi-Axis Synchronization: Computes duration T_max across all axes, then scales velocities and accelerations so all axes arrive simultaneously.

## Slide 8
CAPSTONE PROJECT | DOMAIN 5
Stage 5: High-Speed IPC & Real-Time Safety Watchdog
POSIX Shared Memory Telemetry Buffer
• Zero-Copy Architecture: Uses shm_open() and mmap() on /dev/shm/motor_hub_telemetry.
• Low Latency: Telemetry packet read in < 2.1 µs.
• Memory-Aligned Packets: Cache-aligned (alignas(64)) to prevent false sharing between CPU cores.
• Asynchronous Command Queue: Dedicated channel for operator move/home/estop commands.
Failsafe Watchdog Supervision
• Heartbeat Timeout: Monitors periodic loop deadlines; missing 150 ms deadline triggers instant E-Stop.
• Tracking Error Threshold: Detects stalls or encoder disconnects if |target - actual| > 35,000 ticks.
• Thermal Trip: Protects actuators if temperature exceeds 80°C.
• Instant E-Stop: PWM dropped to 0 in < 0.05 ms upon trip.

## Slide 9
CAPSTONE PROJECT | DOMAIN 5
Stage 5 & 6: Verification & Performance Benchmarks
Pick-and-Place Trajectory Simulation Results
• 4-Waypoint Sequence: Approach -> Lower End-Effector -> Grip & Lift -> Traverse to Place.
• Total Simulated Time: 4.202 seconds (4,201 discrete 1 ms cycles).
• Simulation Speedup: 186.0x real-time execution in automated verification.
• Steady-State Accuracy: Settled within deadband (Axis X: 0.16 ticks, Axis Y: 4.77 ticks).
• Safety Cutoff: E-Stop PWM dropped to 0 instantly on simulated fault.
System Performance Metrics
• Periodic Loop Rate: 1000 Hz (1.0 ms deterministic period).
• Loop Computation Time: 24 µs / cycle (6.25x headroom under 150 µs budget).
• E-Stop Reaction Time: < 0.05 ms to zero PWM output.
• Shared Memory Latency: < 2.1 µs zero-copy transfer.
• Memory Footprint (RSS): 4.8 MB (70% below 16 MB limit).
• Automated Test Coverage: 100% Pass across all unit and integration tests.

## Slide 10
CAPSTONE PROJECT | DOMAIN 5
Stage 6: Demonstration & Operator CLI Interface
Interactive Operator CLI (motor_cli)
• status: Displays live ASCII telemetry table (Positions, Velocities, PWM, Temperatures).
• move <axis> <ticks>: Commands single axis movement.
• sync <x> <y> <z>: Executes synchronized 3-axis Cartesian movement.
• home <axis>: Homing routine with limit-switch zeroing.
• monitor: Auto-refreshing 10 Hz live dashboard.
• estop / clear: Instant emergency stop and fault reset.
Deployment Flexibility
• Native Linux / WSL2: Loads motor_hub_driver.ko kernel module with real character device /dev/motor_hub.
• Mock Emulation Mode: Runs daemon on any machine with --emulation flag without root permissions.
• Automated Cross-Platform Simulation: Runs scripts/simulate_and_verify.py on Python 3 anywhere.
• Pre-Configured VS Code: Full IntelliSense and one-click build tasks (Ctrl+Shift+B).

## Slide 11
CAPSTONE PROJECT | DOMAIN 5
Stage 6: Achievements, Limitations & Future Roadmap
Key Achievements
• Executed full 6-stage engineering lifecycle from PRD to final delivery.
• Demonstrated Linux kernel driver, real-time POSIX programming, and C++ OOP.
• Sub-millisecond determinism (24 µs loop latency).
• Complete Git version history tracking each milestone on GitHub.
Technical Limitations
• Physical Silicon Dependency: Hardware tests performed via high-fidelity register emulation.
• Trajectory Dynamics: Uses trapezoidal velocity profiling rather than 7-phase jerk-limited S-curve.
• Fieldbus Isolation: Direct MMIO driver rather than industrial fieldbus.
Future Roadmap
• EtherCAT / CANopen HAL: Integrate SOEM stack for distributed servo amplifiers.
• ROS 2 Integration: Build a ros2_control hardware interface plugin.
• Hardware Acceleration: Offload PID and register maps to a RISC-V FPGA coprocessor.

## Slide 12
Thank You!
Questions & Discussion
Robotic Multi-Axis Motor Controller & Actuator Hub
• Repository: https://github.com/Amankumar307/robotic-motor-hub
• Deliverables: Linux Kernel Driver | 1 kHz RT Daemon | Dual HAL | Full 6-Stage Reports | 100% Tests Passed